## Slide 1: Heavy Water Cooled Thorium Breeders and Static Molten Salt Breeder
Naoyuki Takaki
Department of Nuclear Safety Engineering

## Slide 2: Contents
Why thorium breeder?
Three concepts
  D2O cooled thorium thermal breeder (CANDU type)
  D2O cooled thorium fast breeder (PWR type)
  Static molten salt breeder (Moltex type)
Proliferation concerns
Conclusions

## Slide 3: Why breeder ?
Chart: Conversion ratio / Breeding ratio
| 0.5 | 0.52 | 0.54 | 0.56000000000000005 | 0.58000000000000007 | 0.60000000000000009 | 0.62000000000000011 | 0.64000000000000012 | 0.66000000000000014 | 0.68000000000000016 | 0.70000000000000018 | 0.7200000000000002 | 0.74000000000000021 | 0.76000000000000023 | 0.78000000000000025 | 0.80000000000000027 | 0.82000000000000028 | 0.8400000000000003 | 0.86000000000000032 | 0.88000000000000034 | 0.90000000000000036 | 0.92000000000000037 | 0.94000000000000039 | 0.96000000000000041 | 0.98000000000000043 | 1.0000000000000004 | 1.0200000000000005 | 1.0400000000000005 | 1.0600000000000005 | 1.0800000000000005 | 1.1000000000000005 | 1.1200000000000006 | 1.1400000000000006 | 1.1600000000000006 | 1.1800000000000006 | 1.2000000000000006 | 1.2200000000000006 | 1.2400000000000007 | 1.2600000000000007 | 1.2800000000000007 | 1.3000000000000007 | 1.3200000000000007 | 1.3400000000000007
回収ロス 1% | 1.1881 | 1.2366 | 1.2892 | 1.3465 | 1.4091 | 1.4778 | 1.5536 | 1.6376 | 1.7311 | 1.836 | 1.9544 | 2.0891 | 2.2438 | 2.4233 | 2.6339 | 2.8846 | 3.1881 | 3.5629 | 4.0377 | 4.6584 | 5.5046 | 6.7265 | 8.6455 | 12.0968 | 20.1342 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5 | 87.5
回収ロス 3% | 1.165 | 1.2107 | 1.26 | 1.3135 | 1.3717 | 1.4354 | 1.5053 | 1.5823 | 1.6676 | 1.7626 | 1.8692 | 1.9894 | 2.1262 | 2.2831 | 2.4651 | 2.6786 | 2.9326 | 3.2397 | 3.6188 | 4.0984 | 4.7244 | 5.5762 | 6.8027 | 8.7209 | 12.1457 | 20 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70 | 70
回収ロス 5% | 1.1429 | 1.1858 | 1.232 | 1.2821 | 1.3363 | 1.3953 | 1.4599 | 1.5306 | 1.6086 | 1.6949 | 1.791 | 1.8987 | 2.0202 | 2.1583 | 2.3166 | 2.5 | 2.7149 | 2.9703 | 3.2787 | 3.6585 | 4.1379 | 4.7619 | 5.6075 | 6.8182 | 8.6957 | 12 | 19.3548 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333 | 58.3333
Chart: Averaged burnup [%]
| 1 | 2 | 5 | 7 | 10 | 15 | 20 | 30
0.1 | 90.9918 | 95.3289 | 98.1354 | 98.6888 | 99.108 | 99.4365 | 99.6016 | 99.7672
0.5 | 66.8896 | 80.3213 | 91.3242 | 93.7709 | 95.6938 | 97.2447 | 98.0392 | 98.8468
1 | 50.2513 | 67.1141 | 84.0336 | 88.2724 | 91.7431 | 94.6372 | 96.1538 | 97.7199
2 | 33.557 | 50.5051 | 72.4638 | 79.0068 | 84.7458 | 89.8204 | 92.5926 | 95.5414
5 | 16.8067 | 28.9855 | 51.2821 | 60.0858 | 68.9655 | 77.9221 | 83.3333 | 89.5522
Recovery loss
1 [%]
3[%]
5[%]
Breeder
JSFR
Monju
Converter
Burner
CR>1
Averaged burnup : 7%
CR<1
U-235 enrichment: 5%
Burnup: 5%
CR vs U utilization factor
BU vs U utilization factor for FBR

## Slide 4: Pros and Cons of MSR
Pros
Low pressure and high B.P.
Burnup is not limited by irradiation damage
Coolant = Fuel → simplified shutdown and decay heat removal
No need for fuel fabrication
Cesium and Iodine stable within fuel salt
etc.
Cons
Fuel salt circulates through whole primary system
Integrity of heat exchanger (Achilles heel)
Materials and chemistry in high temperature circumstance
Loss of delayed neutrons
Large neutron absorption by salt
etc.

## Slide 5: Incentives
Why water cooled / oxide fuel?
  well-established plant / fuel technology
Why thorium ?
  Breeding potential in fast/thermal spectrum with negative void effect
  No severe energetics during CDA
  Diversify fission energy resource
  Smaller MA production
http://thorenergy.no/

## Slide 6: Contents
Why thorium breeder?
Three concepts
  D2O cooled thorium thermal breeder (CANDU type)
  D2O cooled thorium fast breeder (PWR type)
  Static molten salt breeder (Moltex type)
Proliferation concerns
Conclusions

## Slide 7: Heavy Water Cooled Thermal Breeder
Fissile number density
Low 233U enrichment
in Th-U oxide fuel
meets breeding condition

## Slide 8: Fuel Bundle Designs
1
2
3
Sustainer
Sustainer
+ Pu burner
Nat.U supported
233U breeder
Discharged burnup | 3.9 GWd/t | 7.9 GWd/t | 2.9 GWd/t
Compound system doubling time (CSDT) | 729 years | 206 years | 13 years
233U enrichment: 1.4%
233U enrichment: 1.4%
Pu enrichment: 2.5%
233U enrichment: 1.4%

## Slide 9: Contents
Why thorium breeder?
Three concepts
  D2O cooled thorium thermal breeder (CANDU type)
  D2O cooled thorium fast breeder (PWR type)
  Static molten salt breeder (Moltex type)
Proliferation concerns
Conclusions

## Slide 10: Heavy Water Cooled Fast Breeder
233U-Th fuel (282)
D2O reflector (96)
B4C control rod (19)
Fuel pin cell
(MFR≒1.0)
(Moderator to fuel volume ratio)
Top view of
PHWBR core
(PHWBR: Pressurized Heavy Water Breeder Reactor)
Hexagonal fuel assemblies

## Slide 11: Neutron Spectrum
Chart: Neutron Energy [eV]
 | Fast fluence | Limitation
Zircaloy-4 | 2.87×1022 | < 1.5×1022
SiC | 2.88×1022 | < 8.0×1022
Zircaloy
SiC
UOX LWR
U-Pu FBR
Th-U233 PHWBR
Unit: n/cm2

## Slide 12: Performances
Similar output (1.3GWe) and core size (<4m) with current PWR
Homogeneous, hexagonal tight pin pitch core (MFR=0.6)
Breeding (BR>1.05) with negative void reactivity coefficient
Higher burnup than LWR (>70GWd/t)
Acceptably small fissile/HM inventory (15ton/200ton)
SiC cladding suited for ATF and high fast neutron fluence

## Slide 13: Deployment Scenario
?
UOX Fuel
Fabrication
LWR
Natural
uranium
Reprocessing
Disposal
Current phase
Thorium
(Th,U-233)O2 Fuel
Fabrication
(Th,U-233)O2 Fueled
PHBR
Reprocessing
Disposal
Th/U-233
Sustainer phase
Pu
Thorium
(Th,Pu)O2 Fuel
Fabrication
(Th,Pu)O2 Fueled
PHBR
Reprocessing
Disposal
Th/Pu
U-233
Transition phase

## Slide 14: Replacement of U-LWRs by Th-PHWBRs
Chart: Years
①U-LWR
②Th-Pu PHWBR
③Th-233U PHWBR
②＋③
60GWe U-LWRs can be replaced within a century.
Constant total capacity

## Slide 15: Cost Impact
Cost reduction factors | Cost increase factors
No need for enrichment (vs. LWR) | Heavy water coolant (vs. LWR)
Proven PWR plant technology (vs. FBR) | Tritium production (vs. LWR)
Less expensive resource (vs. UO2 fuel) | Challenging reprocessing technology (vs. UO2 fuel)
 | High gamma fuel handling (vs. UO2 fuel)

## Slide 16: Generation Cost of PHWBR
Chart: Generation cost [yen/kWh]
| Low | Nominal | High
Fuel cost | 0.75 | 0.95 | 1.15
Capital cost | 1 | 1.6 | 1.9
O&M cost | 0.8 | 1.4 | 1.75
LWR (5.3 yen/kWe)
Plant : 1300MWe PWR
Evaluated by FEPC in 2004.
FBR (2.6 yen/kWe)
Plant : 1500MWe MOX-FBR
Evaluated by JAEA in 2010.

## Slide 17: Contents
Why thorium breeder?
Three concepts
  D2O cooled thorium thermal breeder (CANDU type)
  D2O cooled thorium fast breeder (PWR type)
  Static molten salt breeder (Moltex type)
Proliferation concerns
Conclusions

## Slide 18: Static Molten Salt Reactor

## Slide 19: Core specifications of SMSR

## Slide 20: Parasitic neutron absorbers

## Slide 21: Modifications to SMSR
Chart: Burnup [GWd/t]
| 0 | 8.90011E-2 | 0.44500599999999996 | 0.890011 | 1.3350199999999999 | 2.6700300000000001 | 4.4500600000000006 | 6.2300800000000001 | 8.9001099999999997 | 13.350200000000001 | 22.250299999999999 | 35.6004 | 53.400599999999997
Pu30wt%(ref) | 1.0298 | 1.0296 | 1.0286 | 1.0274 | 1.0271 | 1.0245 | 1.0209 | 1.0179 | 1.0134 | 1.0067 | 0.99191 | 0.97162 | 0.94647
Cl濃縮Pu27wt% | 1.0454 | 1.0438 | 1.0434 | 1.0432 | 1.0418 | 1.0385 | 1.0361 | 1.0339 | 1.0293 | 1.0221 | 1.0082 | 0.98908 | 0.96716
SFNC | 1.0051 | 1.0052 | 1.0044 | 1.005 | 1.0073 | 1.0103 | 1.0152 | 1.0195 | 1.0155 | 0.99654 | 0.9571 | 0.92072
Reference core (SSR)
Pu enrichment： 30wt%
Cl-37 enriched core
Pu enrichment： 27wt%
Cl-37 enriched + Na cooled core
Pu enrichment： 15wt%
Chlorine composition : Natural → Enriched Cl-37
(to reduce absorption)
Coolant material : Fluoride salt → Sodium (to mitigate spectrum softening)
Z
18
17
16

## Slide 22: Performances
Chart: Burnup [GWd/t]
| Reference core (SMSR) | Cl-37 enriched core | Cl-37 enriched + Na cooled core
Burnup [GWd/t] | 17 | 28 | 134
Conversion ratio* | 0.68 | 0.77 | 1.07
Chart: Pu breeding gain [kg/GWt/y]
| Reference core (SMSR) | Cl-37 enriched core | Cl-37 enriched + Na cooled core
Pu breeding [kg/GWt/y] | -84 | -39 | 67
MA production [kg/GWt/y] | -14 | -19 | -13

## Slide 23: Contents
Why thorium breeder?
Three concepts
  D2O cooled thorium thermal breeder (CANDU type)
  D2O cooled thorium fast breeder (PWR type)
  Static molten salt breeder (Moltex type)
Proliferation concerns
Conclusions

## Slide 24: Proliferation Concerns of U-233
 | Gamma dose | Critical mass | Enrichment technology | Implosion technology | Heat production
U-235 | None | 48kg | Required | Not required | None
Pu (Weapon grade) | Low | 10kg | Not required | Required | Low
U-233 (Low grade) | High | 16kg | Not required | Not required | Low

## Slide 25: Conclusions
CANDU type thorium thermal breeder is the most promising for near term introduction if commercial reprocessing technology is developed.
PWR type thorium fast breeder base on proven technologies can be deployed as dominant energy sources within a century.
Static molten salt reactor requires Cl-37 enriched fuel salt and sodium coolant to be a breeder.

## Slide 26: What I want to share
Breeding is the key for sustainable society.
Thorium shows some preferable characteristics but is not magic fuel, basically the same as uranium.
Thorium reactor produces similar nuclear wastes if the cycle is not closed.
Closing cycle just minimizes the wastes and maximize the resources regardless of U or Th.