## Slide 1: The ThorMer Reactor A nuclear power plant with no moving parts
Jonathan Schattke
Missouri University of Science and Technology

## Slide 2: Design Overview
Accelerator Driven – subcritical, no control rods, energy multiplication
Thorium – cheap, abundant, used in natural form
Mercury – dense, liquid at room temperature, shielding, spallation target & coolant
MagnetoHydrodynamic Generation – no turbines
Natural pressurization – gravity head, no pump

## Slide 3: Accelerator Driven Energy
High flux proton beam
Heavy Metal Target – Metal for heat removal
Design Basis: 300 MeV [beam efficiency] protons, mercury target, ~3.4 neutrons per proton
Safety: beam off = scram; target gone = scram (keff drops with just fission neutrons)
1/(1-keff) multiplication of neutrons
Final: (3.4/0.3)*0.2/(1-keff); 0.95 keff = 40x Thermal out vs. Beam in

## Slide 4: Thorium Fuel Cycle
Many times more abundant the Uranium
Long fuel load times; 10 year core without reloading
Breed in Fast, Epithermal and Thermal reactors
Available in almost all countries, no need for international agreements

## Slide 5: Mercury Coolant
Low viscosity
356 °C Boiling point at 1 Atm; temperature range well understood
High σa, not suitable for channel type coolant in large reactors
Very small reactors (Clementine), mercury is integral neutron and gamma shielding
Dissolves many metals – fission products from fuel failure kept in solution in accident

## Slide 6: MHD Generator
Magneto-Hydrodynamic Generation based on current passing through a coil F=Q∙(vˣB)
Requires charge in kinetic stream; provided by Helicon coil
Monatomic gasses best
Kinetic Energy directly converts to Electric Current

## Slide 7: 3m Core Layout
Pu/Th mix HM until U233 inventory built up
Thorium metal in corners to enhance breeding for additional reactors
MgF salt in solid phase
Heat removed at surface by boiling mercury
No internal structure

## Slide 8: Neutron Spectrum
Extremely Fast Spectrum – spallation neutrons up to beam energy, Fluorine lightest element at load
MgF2 low lethargy per collision, 3.5 cm mean free path
Cell 17: 5-15 cm Cell 317: 45-75 cm
Cell 117: 15-25 cm Cell 417: 75-100 cm
Cell 217: 25-45 cm Cell 5xx: 100-150 cm

## Slide 9: Breed calculations
Seed is reactor grade Pu
Breed from Thorium maintains steady keff for 10 years
Total HM: 96.2 Tons Load Fissile Inventory: 1071 kg
146 GWD in calculation BR: 0.998

## Slide 10: Summary
300 MeV 1 MW Proton beam costing 3 MWe
Mercury spallation produces 3.4 neutrons
Pu/Th subcritical assembly produces 40 MWth in Mercury steam
Mercury Steam produces ~15 MWe in Magnetohydrodynamic Generator
Condenser maintains pressure differential
Condensate flows back to core